## Slide 2: What is D’oH?
D’oH is an automated dough making machine. Its purpose is to make the baking process easier by removing the need to measure ingredients by hand.
D’oH היא מכונה המכינה בצק בצורה אוטומטית. מטרתה היא להפוך את תהליך האפייה לפשוט ומהיר יותר ע"י הסרת הצורך במדידה ידנית של חומרי הגלם.

## Slide 3: HARDWARE
The hardware is based on the following main components:
  The rail
  The scale
  The containers
  The hall effect.
  The relay module.
  The solenoid valve.

## Slide 4: HARDWARE
  We’ve created a working stepper-motor based rail. The rail is controlled by a stepper motor, which is in return controlled by Bluetooth commands.
  We’ve created 3D printed dispensers for the small and large containers, each dispenser is controlled by a servo motor.
  We’ve created a working weight scale using a 5kg load cell.
  We’ve created a bowl detector using a hall effect sensor.
  We’ve created a working valve for the liquid containers using a solenoid valve controlled by a 2-channel relay module.
  The rail, the hall effect sensor and the scale are controlled by a master Arduino and the containers and valves are controlled by a slave Arduino using I2C.

## Slide 5: SOFTWARE
Login Page
  User must insert username and password, if not an error message appears.
  The username and password are checked against the users database, through a function app in the cloud.
  The user has a finite amount of login attempts before his user is locked for a finite amount of time.
  The user can select “Forgot password?” and his password would be reset and sent to him via email.
  If the log in is successful, the application tries to the previously selected Bluetooth device. If it fails, the users can skip ahead or stay in the same screen.

## Slide 6: SOFTWARE
Signup Page
  To sign up for app (the users database) with a new account, the user must insert: username, email, password and password verification.
  The password must be at least 6 characters long and must contain at least one capital letter and at least one digit.
  The password and the password verification fields must match.
  Username can not be an existing username in the database.
  Email can not be an existing email account in the database.
  Once the users pressed on “Register”, the account is created and added to the database in the cloud using function apps. Then, the user is directed to the Select Bluetooth Device Page, and from there he is directed to the Configure Containers Page.

## Slide 7: SOFTWARE
Main Page
  Created of 4 tabs – Main, Stats, History and Settings.
  Main Tab:
    Contains the 3 latest recipes that the user created (whether he just saved the recipe or made the dough using the recipe).
    The user can select one of those recipes and move to the Recipe Page, or select “New Recipe” to create a new recipe, or logout.
  Stats Tab:
    Shows the current amount of material for each of the containers.
  History Tab:
    Shows all the recipes that the user ever made from newest to oldest.
    User can select any of these recipes and go to the Recipe Page.
  Settings Tab:
    User can select:
      Configure Containers- will lead to Configure Containers Page where user can select which ingredient is in which container and it’s amount.
      Add To Containers – will lead to Add To Containers Page, where the user can only add amount to an existing ingredient.
      Select Bluetooth Device – will lead to Select Bluetooth Device Page.

## Slide 8: SOFTWARE
Recipe Page
  This page is the same for selecting an existing recipe or creating a new one.
  The user can set/change the name of the recipe.
  The user can select the ingredients in the recipe- the first 3 ingredients in the list are “big container” ingredients that can be chosen using a picker, the following 3 ingredients are “small container” ingredients that can be chosen using a picker, and the last 2 are currently only water and oil (what our machine can support so far).
  For each ingredient, the user can choose an amount and a measurement unit (cup, gr, tsp or tbsp). Liquids can only be measured in cups, the big containers can be measured by gr or cup, and the small ingredients can only be measured by tsp or tbsp.
  The conversion between measurements is done through the app using the conversion table which is stored and loaded from the cloud using a function app.
  The user has 2 options- Let’s D’oH! which first saves the recipe to the user’s recipes database and then sends the command to the machine and moves to the Progress Page. The second option is Save Recipe, which saved the recipe to the user’s recipes database and then returns to the Main Page.
  If the user chooses an amount that is greater than the amount in the containers, or chooses an ingredient that doesn’t exist, once he presses the Let’s D’oH! button an error message appears and the user is left in the same page.

## Slide 9: SOFTWARE
Progress Page:
  Shows the progress of the machine.
  If the bowl is removed from the scale during the process an error message appears asking the user if he wishes to continue or to stop. In order to continue the user must set the bowl back on the scale.
  Once each station (container) is cleared the final amounts in the containers are updated- big containers by the weight collected by the scale for each big ingredient, and the rest by the amount the user entered (because it works on set ingredient volumes and not on weight).
  If the required weight for a big ingredient is not achieved (i.e the hatch of the container is stuck, and the ingredient no longer falls out) the machine stops its process and returns to the first station. The application goes back to the recipe page and the amount are updated according to the stations that already finished.

## Slide 10: CLOUD
The cloud holds 4 main databases:
  Users database
  Ingredients database
  User Recipe database
  Containers database
The Containers Database is made up of 8 separate databases, one for each container.
The cloud also holds all the functions apps that connect the app commands to the databases in order to avoid corruption and vulnerability of the databases.

## Slide 11: CLOUD
Function Apps:
  UserLogin- receives a user (username, email, password) from the application and returns the user’s ID if the user is valid and exists. Otherwise returns 0 (IDs start from 1).
  UserRegister- receives a user (username, email, password) from the application, inserts the user into the users database if he does not already exist, and returns its unique user ID. If the user already exists, returns 0.
  UsernameExists- receives a username from the application, checks if the username exists in the users database, if he does returns its unique user ID, otherwise, returns 0.
  EmailExists- receives an email from the application, checks if the email exists in the users database, if he does returns its unique user ID, otherwise, returns 0.
  GetUserBuID- receives a unique user ID from the application, checks if the ID exists in the users database, if he does returns its user details (username, email, password), otherwise, returns 0.
  GetUserRecipe – receives user ID and returns the recipes that belong to that user from the Recipe Database.
  AddUserRecipe – receives a recipe and user ID and adds it to the Recipe Database.
  GetConvTable – returns all possible ingredients and their conversion factors.
  GetContainers – receives a user ID and returns that user’s container ingredients and current amounts.
  SetContainers – receives a user ID and a list of the containers (ingredients and amounts) and inserts them to the user’s containers database.